## Slide 1
WildFire
Paul Duszak Jessica Oberg
Xin Qu
Tony Sarles
Terry Schmidt
Peter Swantek

## Slide 2
Microsoft Azure
  Web services
Node.js
  Web server
  Backend API
Sequelize
  Object-Relational Model for Node.js
  Using instead of SQL to set up database schema
MySql
  The flavor of SQL we decided to use for this project
Libelium WASPMOTE
  The hardware
Technology Used

## Slide 3
Hardware
Waspmote
  Open source sensor platform
  Modular architecture: Allows for using only desired modules or sensors
Gas Sensor Board
  Integrates into the Waspmote, designed to monitor environmental parameters
  Allows inclusion of sensors (up to 6) that will measure different gases to allow for quantification of an area's air quality

## Slide 4
Hardware (cont.)
Waspmote Gas Sensor Board and Sensors

## Slide 5
Interface With Hardware
Program is developed and uploaded to the Waspmote
Initial setup
  Will only execute one time
  Turn on Gas Board, initialize individual sensors
Main loop
  Portion of the program that will loop continuously
  Will perform data gathering and transmission here
  Turn everything off and go to sleep for determined amount of time

## Slide 6
Interface With Hardware (cont.)
Our current set up
  Turn on the Gas Sensor Board
  Initialize each sensor that will be used for measurement
Our current loop
  Let sensors warm up before taking measurements
  Gather the raw data that is output by each sensor (output is a voltage)
  Convert the raw voltage output from each sensor into an actual gas concentration (parts per million, ppm)
  Package the data and transmit to our mobile app to be ultimately pushed to our web server
  Put the board to sleep, wake up after a determined time to perform another loop

## Slide 7
Interface With Hardware (cont.)

## Slide 8
Android Interface

## Slide 9
Web Interface

## Slide 10
Next Steps & Challenges
Upcoming development goals
  Currently have 2 gas sensors: Carbon Dioxide (CO2) and Carbon Monoxide (CO); will be integrating additional sensors for Ozone (O3) and Nitrogen Dioxide (NO2)
  Add Bluetooth functionality for communication with a mobile phone/device
Current challenges
  Initializing sensors with correct parameters, somewhat trial and error
  Optimizing the time of sensor warmup and sleep cycle
  Deriving equations to convert raw sensor data to a meaningful gas concentration
  Certain gas concentrations may be below the respective sensor's sensitivity level

## Slide 11
Next Steps & Challenges
Upcoming development goals
  Add user account functionality to secure API endpoints and increase accountability
  Connect android application to web API
  Integrate web map and Android app
Current challenges
  Two separate code bases for web map and android map → double work load
  PHP and MySQL queries will be rewritten in javascript